## Slide 1: Multimetallic Systems Convey Cost-Effective Hydrogen Storage
L.P. Matte, M. Jaugstetter, A.S. Thill, T.P. Mishra, C. Escudero, G. Conti, F. Poletto, S. Nemsak, and F. Bernardi, ACS Nano 19, 10 (2025). doi: 10.1021/acsnano.4c18013. Work was performed at ALS/LBNL and Molecular Foundry/LBNL.
Scientific Achievement
A bimetallic material (Pd-Ni) produces hydrogen-active nanopockets that improve the efficiency and lower the cost of hydrogen storage systems.
Significance and Impact
Mechanistic understanding of a Pd-Ni bimetallic system paves the way to design cost-effective hydrogen storage, opening new opportunities to develop reliable energy technologies for the energy industry.
Research Details
  Ambient-pressure x-ray photoelectron spectroscopy (APXPS) and grazing-incidence x-ray scattering (AP-GIXS) at the Advanced Light Source (ALS) and transmission electron microscopy and electron energy loss spectroscopy at the Molecular Foundry revealed morphological and chemical changes of the samples.
  In the bimetallic system, nanoparticles with a significantly lower concentration (25%) of Pd produced more pockets, thereby increasing hydrogen storage capacity while lowering the total cost.
A nanoparticle composed of a Pd core (red) and NiO shell (yellow) (left). At normal temperature and ambient pressure, the Pd atoms migrate to the surface of the nanoparticle, opening pockets in the Pd core where hydrogen (white) bonds with the Pd (right).
Notes: A bimetallic material (Pd-Ni) produces hydrogen-active nanopockets that improve the efficiency and lower the cost of hydrogen storage systems. Mechanistic understanding of a Pd-Ni bimetallic system paves the way to design cost-effective hydrogen storage, opening new opportunities to develop reliable energy technologies for the energy industry.
Researchers: L. P. Matte (Instituto de Física, Universidade Federal do Rio Grande do Sul, Brazil and ALS); A. S. Thill, F. Poletto, and F. Bernardi (Instituto de Física, Universidade Federal do Rio Grande do Sul, Brazil); M. Jaugstetter and T. P. Mishra (Berkeley Lab); C. Escudero (ALBA Synchrotron Light Source); and G. Conti and S. Nemsak (ALS, University of California, Davis).
Funding: Research Support Foundation of the State of Rio Grande do Sul (FAPERGS), the Brazilian National Council for Scientific and Technological Development (CNPq), the Brazilian Coordination for the Improvement of Higher Education Personnel (CAPES), the Spanish Ministry of Science and Innovation (MICINN-FEDER), and US Department of Energy, Office of Science, Basic Energy Sciences program (DOE BES), Catalysis Research Program. Operation of the ALS and Molecular Foundry are supported by DOE BES.
Publication: L.P. Matte, M. Jaugstetter, A.S. Thill, T.P. Mishra, C. Escudero, G. Conti, F. Poletto, S. Nemsak, and F. Bernardi, "Direct Observation of Phase Change Accommodating Hydrogen Uptake in Bimetallic Nanoparticles,” ACS Nano 19, 10 (2025), doi: 10.1021/acsnano.4c18013.
Full highlight: https://als.lbl.gov/multimetallic-systems-convey-cost-effective-hydrogen-storage